## Slide 1
The New
Millenium
®
2025

## Slide 2
Discover the evolution
Integrated Ethernet port TCP/IP
Read more
x2
Doubled internal memory
Read more
Read more
Modbus RS-485 port optional
I / O
Read more
Up to 60 inputs/outputs
Read more
Memory interface with SD card
Read more
3-color display on 6 lines
Read more
Webserver

## Slide 3
PROGRAMM TRANSFER
Millenium 3 Soft to Crouzet Soft
Software upgrade with new features
Download and install Crouzet soft available on Crouzet.com
A more intuitive user interface
A simple 4-step transition:
Open your existing program
3
Select the equivalent controller
2
Adapt inputs/outputs and edit
4
Download the transition kit
1

## Slide 4
Detailed comparison of logic controllers
Millenium 3
New Millenium
1 - COMMUNICATION
2 - INTERCHANGEABLE INTERFACE
3 - INPUTS / OUTPUTS
4 - PROGRAMMING
5 - DISPLAY SPECIFICATIONS
6 - NAVIGATION

## Slide 5
New Millenium
Expansion Ethernet TCP/IP port
Millenium 3
Integrated Ethernet TCP/IP port
RJ45
Built-in Ethernet
No expansion module needed
COMMUNICATION
1

## Slide 6
The 2 models have a memory cartridge
Extend your PLC memory, perform data, or load a new program
Up to 2,000 function blocks
*SD card not included
Modbus RS 485 available on base thanks to an interface
x2
Doubled internal memory
MEMORY CARD
RS 485
New Millenium
Millenium 3
MODBUS RS 485 & SD card interface
INTERCHANGEABLE INTERFACE
2

## Slide 7
Digital
Analog
High-speed
4 - 20 mA
x12
Add up to 12 expansion modules*
Multiple Input Types
mA
Up to 60 I/Os
INPUTS / OUTPUTS
3
*please refer to the datasheet or configurator to find your solution
Relays
SSR / PWM
Outputs

## Slide 8
Digital
Analog
High-speed
4 - 20 mA
x12
Add up to 12 expansion modules*
Multiple Input Types
mA
Up to 60 I/Os
INPUTS / OUTPUTS
3
*please refer to the datasheet or configurator to find your solution
Relays
SSR / PWM
Outputs

## Slide 9
2 programming modes
PROGRAMMING
4
Visual Function Block programming
Transfer multiple programs at once
Ladder, front face programming
More than 2000 FBD (5 times more than market leader)
SD card, Laptop and cable

## Slide 10
Improved visualization
DISPLAY SPECIFICATIONS
5
6 lines 24 characters/line 3 colors
New Millenium
Status color changing screen : White, green or orange to easily identify alarm and alert status
4 lines 18 characters/line 1 color
Millenium 3
New display More information Tri-color screen

## Slide 11
*SD card not included
Same buttons, new usability
NAVIGATION
6
A
B
ESC
OK
A
B
Easy access to your data and process thanks to our new navigation interface
New Millenium
Millenium 3

## Slide 12
PRODUCT SETTINGS
Access to a webserver
Monitor at a distance inside your network
Make sure your application is running
Receive alerts
Simplify your maintenance operations

## Slide 13
YOUR CUSTOM-MADE PRODUCT
Design Lab
From simple adaptations to custom designs
LAB
DESIGN
When your application requires more than standard products, our DesignLAB team, with 100+ experts in electromechanics, electronics & software, is ready to partner with you in the development of the best customized solution dedicated to your project.

## Slide 14
Simplify
Modular offer
Simplify range with display or blind versions
All models now expandable
Compatibility
Compatible with existing programs
Upgraded software with new features
A more intuitive interface
M3 Soft
Crouzet soft
What's new
Integrated Ethernet TCP/IP port
Modbus RS-485 port optional
Memory interface on SD card
Doubled internal memory
Up to 60 inputs/outputs
3-color display on 6 lines
Webserver
Easier, Better, Faster, Stronger

## Slide 15
The
Millenium
®
range
view technical details
With display and without display versions
Digital or Analog 35mm / Digital 70mm
New controller 12 I/Os
New expansions

## Slide 16
With display
Without display
New controller 12 I/Os
view expansions
The
Millenium
®
range
DISPLAY
SIZE
SUPPLY
INPUTS
OUTPUTS
Expandable
COMMUNICATION
Datalog
Memory
SOFTWARE
MXD12RU3ET
MXD12RU1ET
MXD12SD1ET
MXD12RD7ET
Tricolor - 6 Lines
70 mm
110-230 V AC/DC
8 Digital
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
Tricolor - 6 Lines
70 mm
24 V AC/DC
8 Digital
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
Tricolor - 6 Lines
70 mm
24 V DC
4 Digital/Analog 4 Digital/HighSpeed
4 SSR/PWM – 0.3A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
Tricolor - 6 Lines
70 mm
12-24V DC
4 Digital/Analog 4 Digital/HighSpeed
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
-
70 mm
110-230 V AC/DC
8 Digital
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
-
70 mm
24 V AC/DC
8 Digital
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
-
70 mm
24 V DC
4 Digital/Analog 4 Digital/HighSpeed
4 SSR/PWM – 0.3A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
-
70 mm
12-24V DC
4 Digital/Analog 4 Digital/HighSpeed
4 Relay - 8A
Yes, up to 60 I/Os
Ethernet, Modbus (with interface)
Yes
Memory Card
MXB12RU3ET
MXB12RU1ET
MXB12SD1ET
MXB12RD7ET

## Slide 17
Digital 70mm
Memory Card Interface
RS485 interface
Digital 35mm
Analog 35mm
New expansions
The
Millenium
®
range
SIZE
SUPPLY
INPUTS
OUTPUTS
70 mm
110-230 V AC/DC
8 Digital
8 Relay
70 mm
24 V AC/DC
8 Digital
8 Relay
70 mm
12-24 V DC
8 Digital
8 Relay
70 mm
24 V DC
8 Digital
8 SSR
35 mm
110-230 V AC/DC
4 Digital
4 Relay
35 mm
24 V AC/DC
4 Digital
4 Relay
35 mm
12-24 V DC
4 Digital
4 Relay
35 mm
24 V DC
4 Digital
4 SSR
MXR16U3
35 mm
12-24 V DC
2 Analog (V/mA)
-
35 mm
24 V DC
-
2 Analog (V/mA)
35 mm
12-24 V DC
2 RTD
-
MXR16U1
MXR16D7
MXS16D1
MXR08U3
MXR08U1
MXR08D7
MXS08D1
MXAI02D7
MXAO02D1
MXAI02PD7
SIZE
SUPPLY
INPUTS
OUTPUTS
SIZE
SUPPLY
INPUTS
OUTPUTS

## Slide 18
2025
For more information visit : www.crouzet.com
THANK YOU FOR YOUR ATTENTION!